## Slide 1
// cross-market probability calibration
CrowdArb
Where the crowd and the professionals disagree — and why it matters.
live crowdarb.streamlit.app repo github.com/Arisrlt46/crowdarb
Aris Rault
SAME EVENT
20%
crowd · Polymarket
0%
professional · CME
gap = 20 pts
crowdarb ▮
Notes: Opening. CrowdArb is a live engine that measures and acts on disagreements between prediction-market crowds and professional financial markets on the same binary events. The panel is the sharpest real example from the project: Polymarket priced a Fed outcome at 20% while the professional futures market implied 0% — a clean 20-point gap.

## Slide 2
// the problem
Two honest markets, one event, different prices
CROWD
Polymarket
Sentiment, attention, and real money — but noisy, and often slow to update on hard data.
PROFESSIONAL
CME · Deribit
Futures and options priced by institutions — disciplined, but not always where the retail crowd is looking.
The disagreement between them is not an error to average away — it is a measurable, tradeable signal.
crowdarb ▮
Notes: Both sources are legitimate but they price the same event differently. Rather than treating the difference as noise, CrowdArb treats the gap itself as the object of interest.

## Slide 3
// the idea
Pair each contract, blend into one fair value
CROWD
get_polymarket_
probability()
PROFESSIONAL
get_professional_
probability()
→
FAIR VALUE
one calibrated
probability
That blended fair value then drives an inventory-aware market-maker and an online calibrator that learns which source to trust.
crowdarb ▮
Notes: For Fed decisions the professional side is CME Fed Funds futures; for crypto price levels it is Black-Scholes on Deribit implied vol. Both are reduced to a probability of the same binary event and blended.

## Slide 4
// architecture
Six layers, one MarketPair interface
0
Data
Extract implied probability from two independent sources
1
Belief
Beta-Bernoulli conjugate updating over order flow
2
Market-making
Avellaneda-Stoikov inventory-aware quotes
3
Calibration
Bayesian model averaging, online Hedge weights
4
News signal
Headline → likelihood ratio → Bayesian update
5
Interpretation
Plain-language readings and scanner labels
crowdarb ▮
Notes: Each layer has a single responsibility and feeds the next. Everything talks to the common MarketPair interface, so the pipeline body has no market-specific logic.

## Slide 5
// layer 0 — probability extraction
Same event, two independent derivations
FED RATES
Algebra on CME Fed Funds (ZQ) futures.
Recover the post-meeting rate from the
month-average rate, then convert to P(cut).
r_after = (r_impl·30 − 17·r_now) / 13
P(cut) = (r_now − r_after) / 0.25
CRYPTO LEVELS
Black-Scholes N(d2) on the asset's price
level, using Deribit's DVOL implied vol
(90-day realized as fallback).
P(reach K) = N(d2)
vol = Deribit DVOL · BTC / ETH
Near month-end the Fed formula switches to the next-month contract to avoid a tiny-denominator blow-up — matching CME's own methodology.
crowdarb ▮
Notes: Layer 0 is the whole point of the project: getting a clean, independent professional probability for the exact same event the crowd is pricing. The Fed side replicates CME FedWatch's algebra from free futures data after CME blocked direct API access.

## Slide 6
// layer 2 — Avellaneda-Stoikov
Inventory-aware quoting cuts P&L variance
−37% to −60%
P&L variance reduction vs naive symmetric quoting
Fed 0.6621 → 0.4145 −37.4% Bitcoin 4.4339 → 1.7658 −60.2%
The maker computes a reservation price and an optimal two-component spread, then shifts its quotes against inventory so it never leans too hard on one side. Less one-sided risk means a tighter, steadier P&L.
crowdarb ▮
Notes: Analogy that works well in the room: the maker treats inventory like a hand of cards it doesn't want too many of — as it accumulates one side, it moves its prices to encourage the other side. That control is what collapses the variance.

## Slide 7
// layer 3 — cross-market calibration
Learn which source to trust, online
up to −9.6%
Brier-score improvement vs the best single source
Fed 0.2186 → 0.2095 −4.1% Bitcoin 0.0112 → 0.0101 −9.6%
Bayesian model averaging with online Hedge weights blends the crowd and professional probabilities, automatically up-weighting whichever has been better calibrated so far. No source is trusted by assumption — it earns its weight.
crowdarb ▮
Notes: Hedge is a classic online-learning algorithm; here the 'experts' are the two probability sources. Over a sequence of resolved events it shifts weight toward the source with the lower loss, so calibration beats either source alone.

## Slide 8
// results — reproducible backtests
Every number is from a fixed-seed backtest
Chart: 
| A-S Fed P&L var | A-S BTC P&L var | Blend Fed Brier | Blend BTC Brier
Improvement (%) | 37.4 | 60.2 | 4.1 | 9.6
METHOD
200-step synthetic price series Fixed seeds: seed=42, p0=0.72 (A-S) seed=7, p=0.30 (blend) Backtest inputs fully disconnected from live data — run twice, identical output.
crowdarb ▮
Notes: Bars are the headline improvements; taller is better. The side panel pre-empts the obvious question — are these reproducible? Yes: fixed seeds and hardcoded starting conditions, no live data leaking into the controlled runs.

## Slide 9
// scanner — real-time auto-discovery
It runs live, and ranks by disagreement
~2,100
live Polymarket markets
swept each refresh
3
market types priced
Fed · Bitcoin · Ethereum
5 min
discovery cache
Refresh clears it
The scanner classifies each contract, keeps only the priceable ones (volume, expiry, and a Black-Scholes sanity band), builds a MarketPair for each survivor, and sorts by the crowd-vs-professional gap — biggest disagreements on top, each with a one-line plain-English read.
crowdarb ▮
Notes: The board is populated entirely by what discovery returns — nothing is hardcoded. The sanity-band threshold is a tunable design parameter, and I flag that explicitly when presenting: the scanner shows a filtered view, not everything that exists.

## Slide 10
// engineering — problems & solutions
The interesting part was the debugging
Month-end blow-up
PROBLEM
A 2-day signal pulled from a 31-day futures average amplified noise ~15.5×, printing a 174% probability.
FIX
Switch to the next-month contract when <5 days remain — CME does the same.
Fake reproducibility
PROBLEM
A "fixed seed" still drifted: the backtest was seeding randomness but pulling its start price from live data.
FIX
Hardcode BACKTEST_P0; disconnect controlled runs from live data entirely.
Scanner sanity band
PROBLEM
Without a filter the board surfaced absurd contracts that broke the blender and the maker.
FIX
Filter to a 0.5–98% BS band; document the threshold as a tunable design choice.
crowdarb ▮
Notes: These are the three I'd want to be asked about. Each has a clean root cause and a fix grounded in how the established industry handles the same edge case. Full write-ups with root-cause analysis are in PROBLEMS_AND_SOLUTIONS.md.

## Slide 11
// the MarketPair interface
Adding a market is ~20 lines
every market implements
get_polymarket_probability() -> float get_professional_probability() -> float metadata() -> dict
run_crowdarb(market) runs Layers 1–5 on any MarketPair with no market-specific logic in the pipeline body.
Write one small class — Fed, Bitcoin, Ethereum today — and the entire engine works on it automatically.
crowdarb ▮
Notes: This is the architectural payoff. The interface is three methods; the pipeline is generic. New assets are a classification-pattern change plus a ~20-line class, not a rewrite.

## Slide 12
// see it live
CrowdArb
A live, explainable read on where the crowd and the professionals disagree.
live crowdarb.streamlit.app repo github.com/Arisrlt46/crowdarb
crowdarb ▮
Notes: Close. Invite them to open the live link — the cold start takes about 15 seconds, so pre-warm it before presenting. Thank the room.